## Slide 1: Low-Cost Precipitation Phase Partitioning Using Acoustic Data and Machine Learning in the Edge
Christian Skalka, Rachael Chertok, Julia Sober. Soheyl Faghir-Hagh, Tian Xia

## Slide 2: Precipitation Phase Partitioning with IoT Sytems
Precipitation phase partitioning: an important, difficult problem for alpine snow hydrology.
  How to detect rain vs. sleet vs. snow with ground-based sensors?
  E.g., Rain on snow detection: one of the 23 unsolved problems in hydrology [1]
Existing sensors (e.g., disdrometers) are expensive and power-hungry.
  Poor spatial resolution- but high spatial variability of phase in alpine settings.
Our approach: Low-cost AI enabled IoT systems, using acoustic sensors.
  Modern platforms (e.g., Arduino) highly programmable, low power/cost.
  Low cost/power/size = better spatial resolution.
[1] Gunter Bloschl, Marc FP Bierkens, Antonio Chambel, Christophe Cudennec, Georgia Destouni, Aldo Fiori, James WKirchner, Jeffrey J McDonnell, Hubert HG Savenije, Murugesu Sivapalan, et al. Twenty-three unsolved problems in hydrology–a community perspective. Hydrological sciences journal, 64(10):1141–1158, 2019

## Slide 3: Low-Cost Arduino Sensor Platform
Phase partitioning can be integrated into a complete snow sensor system (incl. snow depth, temp/rh, others).
Precipitation phase detection, summary:
  Audio data recorded via a microphone.
  Audio features extracted from this audio via signal processing.
  Features provided to ML models, previously trained to classify precipitation phase.
Critical to embed the entire prediction workflow on device.
  Streaming sound data is too costly for remote near-real-time reporting or even storage.
  Smart sampling ensures conservative use of mic.

## Slide 4: Detection Algorithm Flowchart
Microphone
.wav file labeled by precipitation type
Audio Signal in Time Domain
Fast Fourier Transform (FFT)
Short Time Fourier Transform (STFFT)
Extract features from time domain:
Extract Features from frequency domain (spectrogram):
MFCCs
Use as input features to ML models: SVM and Random Forests
Outputs: Classified precipitation phase
Light rain, heavy rain, light hail, heavy hail, snow, silence
If dew point > 100 - e
Yes
No: Wait x minutes, then resample

## Slide 5: Machine Learning Technologies
Models must be able to fit on embedded device (nonvolatile and program memory).
  Rules out deep learning architectures.
Algorithms we’ve evaluated:
  Random Forests
  Support Vector Machines (SVM)
  XGBoost (ruled out, too computationally expensive)
  Logistic Regression (too simple for this data, did not converge)
Signal processing performed to extract audio features:
  Time domain: four possible temporal features.
  Frequency domain: 12 possible spectral features.
  MFCCs: Mel Frequency Cepstral Coefficients.
Insert Image?

## Slide 6: Machine Learning Results with Synthetic Data
Input features to ML models retrieved from synthetic data.
  Rain simulated with large watering can.
  Sleet/hail simulated with poured couscous.
Current model results, on synthetic data, as follows (in percentages):
Power and memory usage: Max ~30mA during prediction workflow, 16KB RAM.

## Slide 7: Current and Future Work
Collecting real weather audio (in process).
Refining models using real data.
Refining hardware for remote IoT-based sensor network deployments.
  Local area networking via LoRA.
  Near real time reporting via satellite uplink.
Integration with full snow hydrology sensor suite:
  Snow depth, soil moisture, temp/RH.

## Slide 8: Supplemental Slides

## Slide 9
ADC
Pin A0
Record .wav files onto the SD card
Read the .wav file from SD
Microphone
Apply Windowing
Discrete
Fourier
Transform
Mel Filter Bank
Log and Discrete Cosine Transform
Calculate and Save MFCCs onto the SD card
Read the MFCC.csv
from SD
Feed the MFCCs to the Random Forest
Model
Results
1. Heavy hail
2. Light hail
3. Heavy rain
4. Medium rain
5. Light rain
6. Snow
7. Silence
MFCC Extraction Flow Chart