## Slide 1: Low-Cost Precipitation Phase Partitioning Using Acoustic Data and Machine Learning in the Edge
Christian Skalka, Rachael Chertok, Julia Sober. Soheyl Faghir-Hagh, Tian Xia

## Slide 2: Introduction
Precipitation phase partitioning: difficult problem to solve (CITE articles?)
Rain on Snow Event detection: one of the 23 unsolved problems in hydrology [1]
Even recording telemetry is a problem:
  Sensors can be expensive: cost, power consumption, and footprint (?-how is footprint different from power consumption?)
Our approach: Low cost AI enabled IoT systems, using acoustic sensors.
Great products w/ good temporal & spatial resolution (Does great products refer to the acoustic sensors? Or the device we’re making?)
[1] Gunter Bloschl, Marc FP Bierkens, Antonio Chambel, Christophe Cudennec, Georgia Destouni, Aldo Fiori, James WKirchner, Jeffrey J McDonnell, Hubert HG Savenije, Murugesu Sivapalan, et al. Twenty-three unsolved problems inhydrology (uph)–a community perspective. Hydrological sciences journal, 64(10):1141–1158, 2019

## Slide 3: Background and Project Description
Previous work performed with AI based phase partitioning using acoustic features
  Classifying rain and rain intensity
Overall Idea:
  Audio recorded via a microphone
  Features extracted from this audio via signal processing
  Features provided to ML models trained to classify precipitation phase
Critical to embed the entire prediction workflow on device
  Streaming sound data is too costly
  Keeping on embedded device enables smart sampling

## Slide 4: Work Flow
Microphone
.wav file labeled by precipitation type
Audio Signal in Time Domain
Fast Fourier Transform
Short Time Fourier Transform
Extract features from time domain:
Extract Features from frequency domain (spectrogram):
MFCCs
Use as input features to ML models: SVM and Random Forests
Outputs: Classified precipitation phase
Light rain, heavy rain, light hail, heavy hail, snow, silence
If dew point > 100 - ∑
Yes
No: Wait x minutes, then resample

## Slide 5: Machine Learning Technologies
Models must be able to fit on embedded device
  Negates use of deep learning (+data requirement)
Models Used:
  Random Forests
  Support Vector Machines (SVM)
  XGBoost (ruled out, too computationally expensive)
  Logistic Regression (too simple for this data, did not converge)
Signal processing performed to extract audio features:
  Time domain: four possible temporal features
  Frequency domain: 12 possible spectral features
  MFCCs: Mel Frequency Cepstral Coefficient
Insert Image?

## Slide 6: Machine Learning Results Using Synthetic Data
Input features to ML models retrieved from synthetic data
Considerations: accuracy vs power & memory needed for model and feature extraction
Current model results, on synthetic data, as follows (in percentages):
If there are any profiling/any other results we want, I think they can go here

## Slide 7: Current and Future Work
Collecting real weather audio
Refining models using real data
Decide on MFCCs vs temporal/spectral features
Refining hardware for remote deployment
  Integration into LoRA network
  Near Real Time Reporting
Insert Image?

## Slide 8: Supplemental Slides

## Slide 9
ADC
Pin A0
Record .wav files onto the SD card
Read the .wav file from SD
Microphone
Apply Windowing
Discrete
Fourier
Transform
Mel Filter Bank
Log and Discrete Cosine Transform
Calculate and Save MFCCs onto the SD card
Read the MFCC.csv
from SD
Feed the MFCCs to the Random Forest
Model
Results
1. Heavy hail
2. Light hail
3. Heavy rain
4. Medium rain
5. Light rain
6. Snow
7. Silence
MFCC Extraction Flow Chart